## Slide 1: INDiC: Improved Non-Intrusive load monitoring using load Division and Calibration
Nipun Batra
Haimonti Dutta
Amarjeet Singh

## Slide 2: Non Intrusive Load Monitoring (NILM)
Breaking down aggregate power observed at meter into different appliances

## Slide 3: Why India?
Different socio-economic settings
How is a residential deployment in India different?

## Slide 4: Deployment Overview
Family characteristics:
  Single family
  3 members
  Medium Income
Home characteristics:
  3 storey
  720 sq. feet

## Slide 5: Deployment Overview: Sensing
Multiple sensing modalities: Electricity, Water, Ambient
Water Energy nexus provides interesting insights

## Slide 6: Electricity monitoring
Smart Meter
Circuit Breaker
Appliance Level
Measuring electricity consumption at Supply, MCB, Appliance
Research questions:
  Value of additional information (and associated cost)?
  What level of invasiveness?

## Slide 7: Water monitoring
Water supply available only for 2 hours in a day
  Pumps used to store water in tanks- Water has EMBEDDED Energy
Instrument the demand and the supply using Pulse based meters
Pulse based water meter

## Slide 8: Ambient sensing
Energy consumption correlated with ambient settings
Measure following ambient parameters
  Light
  Temperature
  Motion
  Sound level
  Bluetooth, WiFi
ZWave Multisensor +Android

## Slide 9: Unique Features in India Unreliable Grid
Voltage fluctuation
Quartile Spread: Less than 1%
Quartile Spread: 9%

## Slide 10: Unique Features in India Unreliable Grid
Voltage fluctuation
Lowest voltage typically seen around midnight- ACs in most home are ON
Highest voltage typically seen early morning

## Slide 11: Unique Features in India Unreliable Grid
2. Blackouts
Observed power outages upto 12 hours a day!
Single power outages of upto 9 hrs observed!

## Slide 12: Unique Features in India Unreliable Grid
3. Learning
System Design: System should be capable of resuming in same state as it was before outage (Batteries way too difficult to manage )
Inferences: Need to measure voltage in addition to current for NILM approaches!

## Slide 13: Unique Features in India Unreliable network- Internet
Observed up to 1/4th packet loss on some days
Learning
Need to account for unreliable internet
Need to do local storage of data
We followed Sense- Local store- Upload

## Slide 14: Unique Features in India Load specifics
Bathroom level water heating-
  Runs off electricity as opposed to gas
  Contributes ~60% of total energy in winters
Room level air conditioning
  Used only in summers
  Control is de-centralized
These two loads are fairly easy to disaggregate- Easy to act upon to reduce energy footprint

## Slide 15: iAWE: Indian Dataset for Ambient, Water and Electricity sensing
2+ months of data
  1 day fully labeled data
  Rest semi-labeled
Electricity, Water, Ambient conditions at different granularities
Dataset released for public use

## Slide 16: iAWE: Indian Dataset for Ambient, Water and Electricity sensing
Dataset explorer

## Slide 17: iAWE: Indian Dataset for Ambient, Water and Electricity sensing
Sample IPython notebooks- Code to interact with data and view results

## Slide 18: iAWE: Indian Dataset for Ambient, Water and Electricity sensing
Entire project maintained as open source on Github
https://github.com/nipunreddevil/Home_Deployment/
https://github.com/nipunreddevil/iawe-website

## Slide 19: Demo
http://energy.iiitd.edu.in:5000/

## Slide 20: Conclusions
Developing countries provide unique challenges for residential deployments
  Unreliable grid
  Unreliable network
  Load specifics
Validated previous work in residential sensing
Release iAWE dataset
“Behind every successful residential deployment, there is a very cooperative (and angry ) family”

## Slide 21: Acknowledgements
NSF- DEITy for funding
Milan Jain (MS IIITD) and Shailja Thakur (MS IIITD) for deployment support
TCS Research and Development for PhD fellowship