## Slide 1: INDiC: Improved Non-Intrusive load monitoring using load Division and Calibration
Nipun Batra
Haimonti Dutta
Amarjeet Singh

## Slide 2: Motivation
Chart: 
| Contribution of buildings to overall energy
India | 47
US | 41
UK | 45
Buildings contribute significantly to overall energy (electricity, gas, etc.) usage
New buildings constructed at rapid rate

## Slide 3: Efficacy of appliance specific feedback
Providing appliance specific feedback to end users can save upto 15% energy.

## Slide 4: Systems for providing appliance specific feedback
Appliance monitors
Provide appliance specific information
Scale poorly
Cost increases with each appliance
Intrusive
Smart meter
Give whole home power information
Information must somehow be broken into different appliances
Non intrusive
Cost effective

## Slide 5: Non Intrusive Load Monitoring (NILM)
Breaking down aggregate power observed at meter into different appliances

## Slide 6: Why NILM works?
Each appliance has a unique signature
This is based on the appliance circuitry
Borrowed from Empirical Characterization and Modeling of Electrical Loads in Smart Homes, Barker et. al

## Slide 7: Key Idea I-Load division
Different loads are assigned to different mains
Smart meter capable of measuring individual mains

## Slide 8: Key Idea I-Load Division
Instead of doing NILM on Mains 1+ Mains 2, as done before, perform NILM on both separately
Intuition:
  Separating out independent components
  Less noise (as noise is distributed too!)
  More scalable

## Slide 9: Key Idea II- Calibration
Different appliance monitors may measure different power for the same appliance

## Slide 10: Key Idea II- Calibration
Power change measured by appliance monitor is significantly lesser than the measurement done at mains

## Slide 11: INDiC
Raw data
Load division
Mains 1 data
Mains 2 data
Processed Mains 1 data
Processed Mains 2 data
Apply NILM
Apply NILM
Calibrate
Calibrate

## Slide 12: Experiments-I Load Division
REDD dataset from MIT
Problem complexity almost halved!
Overall
Mains 1
Dishwasher
Stove
Mains 2
Refrigerator
Kitchen
Microwave
Lighting

## Slide 13: Experiment II Calibration
Before calibration
After calibration
Unaccounted power or noise reduces after calibration
Should improve accuracy

## Slide 14: Combinatorial Optimization (CO) based NILM
Take all possible combinations of appliances in different states and match to total power
Exponential in number of appliances
Load division gives exponential improvements!!
Fan | AC | Total Power (W)
OFF | OFF | 0
OFF | ON | 1000
ON | OFF | 200
ON | ON | 1200
Toy example illustrating CO

## Slide 15: Evaluation Metrics
Mean Normalized Error (MNE)
  Normalized error in energy assigned to an appliance
  Given by |/
RMS Error (RE (Watts))
  RMS error in power assigned to an appliance

## Slide 16: Results
Refrigerator’s accuracy improves significantly
 | State 1 | State 2 | State 3
State 1 | 4740 | 288 | 41
State 2 | 1775 | 2860 | 176
State 3 | 112 | 63 | 25
 | State 1 | State 2 | State 3
State 1 | 4541 | 430 | 98
State 2 | 221 | 4434 | 156
State 3 | 5 | 44 | 151
[i,j] entry:
Number of instances in ith state predicted in jth state
Without INDiC
With INDiC
Refrigerator Confusion Matrix

## Slide 17: Results -II
Appliance | Without INDIC |  | With INDiC | 
 | MNE (%) | RE (W) | MNE (%) | RE (W)
Refrigerator | 52 | 91 | 25 | 67
Dishwasher | 662 | 131 | 73 | 52
Lighting | 176 | 64 | 63 | 43
Both MNE and RE reduce significantly after applying INDiC

## Slide 18: Acknowledgments
TCS Research and Development for supporting Nipun Batra through PhD fellowship
NSF-DEITy for project fund